LoRa Frame architecture

We're at the Radio frenquencies level here i think
Preamble in EU863-870 :
sync word : 0x34 for lora modulation (lenght : 8 symbols)
       0xC194C1 for GFSK (5bytes)

Preamble :
sequence of constants upchirps to cover the whole frequency band
last 2 : sync word -> in order to differentiate 2 lora nwk

Uplink physical message	(We're on physical layer here)
→ sent by end device to the server (by the gw)

Preamble	LoRa Physical Header (PHDR)	PHDR-CRC	PHYpayload / (physical payload)	CRC

PHDR :
Contains payload lenghth in bytes, FEC Code Rate, optionnal 2 bytes CRC of PLD

Let's take a look at PHYPayload

MHDR (MAC header)	MACPayload	MIC (Message Integrity Code)

Size (1o)	1 → M	4o

Decomposition of the MAC header :

Bit number	7..5	4..2	1..0
MHDR bits	Message Type	RFU	Major

Message type

Mtype	Desc
000	Join request
001	Join accept
010	Unconfirmed data UP
011	Unconfirmed data DOWN
100	Confirmed data UP
101	Confirmed data DOWN
110	RFU
111	Proprietary

Then MACPayload

FHDR	FPort	FRMPayload

4 fields in the FHDR (Frame Header) :

DevAddr	FCtrl	FCnt	FOpts

4 bytes	1	2	0..15

DevAddr is the shot address of the device, Fctrl is a frame control octet, Fcnt is a frame counter, and Fopts are frame otions

Let's take a look at the FCTRL field for frames
In case of a downlink frame :

Bit #	7	6	5	4	3..0
Desc	ADR	ADRACKReq	ACK	Fpending	FOptsLen

And for the uplink :

Bit #	7	6	5	4	3..0
Desc	ADR	ADRACKReq	ACK	RFU	FOptsLen

ADR is adaptative data rate . When this bit is set, nwk will control data rate of the end device witch some mac commands. If not, the data rate will stay the same, whatever the signal quality.

ADRACKREQ is used in the specific case the end device is required by the network to use a higer data rate than it's default one. If so, the device needs to check periodically if the network is still receiving its uplink frames
Every new uplink , the device increments an uplink frame counter . If this counter goes over a fixed value without any downlink frames , then the ADRACKREQ bit is set (ADR acknowledgement request bit) . Then the network is required tto send adownlink frame within a set timer.
If that timer is not respected, device will try to switch on a lower data rate (so, higher range) , to try to get connectivity again

ACK : obv, acknowledgement . Used in case of a confirmed data message. Indeed, the receiver have to ack the reception of the message. If sender is a ED , nwk will send the ack using one of the receiving windows opened (//I really need to explain that ⁾

Fpending : down only : if gw has more data to send to the ED

FRAME OPTIONS :

In the Fctrl byte, we have a FOptsLen field which represents the size of the FOpts field in the Frame Header
If set to 0 → no FOpts field
If !=0 → MAC commands are present → Cannot use port 0 (etiher no FPort or !=0)

Port Field :

if the payload file is not empty, need a port field .
FPort value of 0 → only MAC commands in the payload
FPort values 1..223 (0x01..0xDF) → app specific
FPort values 224..255 (0xE0..0xFF) → future apps

RMPayload

Mac Frame Payload Encryption

if payload then FRMPayload needs to be encrypted before ca lculating message integrity code
Encrypted by AES (we'll see that later i guess)
By defalut, encryption is made by Lora layer. Can be done above for specific ports except 0

MIC

//TODO

Random facts that seems like really important :

EU868Mhz Max payload size (depending on the data rate)

Data rate	M
0	59
1	59
2	59
3	123
4	230
5	//
6	//
7	//

Max PL size if ED will never operate with a repeater (need to precise what's a repeater though)

Replace 230 by 250

LoRa Bit rate, Spreading factor and all this stuff

Duration of a Symbol : TS = 2 * SF * BW (SF : spreading factor , BW : BandWidth) ???

Then we can find the useful bit rate Rb = SF*BW2SF*CR (CR : code rate = 4/(4+n), n in [1;4])

 Rb = { [ {4} over {4+ CR} ] } over { { 2^{SF}} over {BW} } times 1000 times SF -> data rate CR in lbrace 1,2,3,4 rbrace SF in lbrace 7,8,9,10,11,12 rbrace

Things about collision risks :
Given that we want to transmit a 24bytes payload. Let's say we're going to do it in SF7, with n without an explicit header on, on only one channel.
W/ header :
On Air time : 62ms
Off Air time : 6100ms

W/out header :
On Air time : 57ms
Off Air time : 5600ms

So theorically, not taking in the equation the reception windows from the ED, we can make around 90 ED transmit without any collision risk. When the first will be done with its off air time,the last will have finished transmitting